## Slide 1: Smart Campus Sustainability & Carbon Footprint Monitoring System
A full-stack IoT + analytics web application (EcoSphere AI)
Yajat M Rawal · S Surendar · Surya Swaminathan · Shivraj Singh
Guide: Dr Arun Nehru J, Assistant Professor, Dept. of CSE (Emerging Technologies)
21CSC203P Advanced Programming Practice · October 2026

## Slide 2: The idea in one slide
Today
Campus checks electricity and water bills once a year
Carbon footprint calculated by hand in Excel
Leaks and AC left on overnight go unnoticed
Our system
IoT meters send readings every minute
Software converts them to CO2 automatically
Algorithms raise alerts within hours
What is measured gets managed.

## Slide 3: Technology stack (100% free and open source)
Frontend
React 19 · TypeScript · Vite · Recharts · Leaflet maps
Backend
Python 3.12 · Django 5 · Django REST Framework · JWT
Database & maths
SQLite (PostgreSQL ready) · NumPy · ReportLab PDFs
IoT layer
ESP32 / smart meters → HTTP JSON API (simulator for demo)
Rs. 0 licence cost · runs on a normal laptop

## Slide 4: System architecture
IoT devices
Energy meters
Water meters
CO2 sensors
Django REST API
Validates data
Carbon engine
Alerts & forecast
SQLite database
Readings
Emission factors
Alerts, users
React web app
Dashboards
Charts & map
Reports
HTTP POST + JSON
Django ORM
REST API + JWT
Labels under the arrows show how each part talks to the next

## Slide 5: Step 1: Collecting sensor data
Every meter sends a small JSON message to our API every minute
POST /api/ingest/
X-Gateway-Key: 6e73...bc69
{
"readings": [
{ "serial": "EM-ACA",
"value": 42.5,
"interval_minutes": 15 }
]
}
Device key
Only registered gateways can send data
Validation
Unknown meter or bad number → rejected
Quality flag
Impossible values stored but marked 'suspect'
Bulk save
Thousands of readings saved in one query

## Slide 6: Step 2: Storing it in the database
Django models (Python classes) become SQL tables automatically
Building
name, type, area, occupants
Meter
serial, kind (power/water)
Reading
time, value, quality
Alert
type, severity, status
EmissionFactor
activity, value, date
User
username, role
1 → many
1 → many
1 → many
About 78,000 hourly readings for 120 days of demo data

## Slide 7: Step 3: Converting energy to carbon
CO2 (kg) = Activity × Emission factor
Worked example
1,000 kWh
electricity used
× 0.716
kg CO2 per kWh (CEA)
= 716 kg
CO2 emitted
Three scopes (GHG Protocol)
1
Fuel we burn: diesel, LPG
2
Electricity we buy
3
Water, waste, commuting
Factors are stored with a 'valid from' date, so updating the CEA value never changes old reports.

## Slide 8: Step 4: Detecting waste automatically
1. Learn normal
Median usage for each hour, from the last 4 weeks
2. Compare
Is this hour far above normal? (robust z-score > 4)
3. Alert
Create a work order with the estimated cost
Result: AC left on overnight in Academic Block B was caught the same night (about Rs. 11,600 wasted per night). All 6 planted faults found, 0 false alarms.

## Slide 9: Step 5: Predicting next month's demand
Inputs
Day of the week
Holidays & vacations
Temperature
Long-term trend
Linear regression
NumPy least squares
Chart: Daily electricity (MWh): actual vs forecast
| 09-26 | 09-27 | 09-28 | 09-29 | 09-30 | 10-01 | 10-02 | 10-03 | 10-04 | 10-05 | 10-06 | 10-07 | 10-08 | 10-09 | 10-10 | 10-11 | 10-12 | 10-13 | 10-14 | 10-15 | 10-16 | 10-17 | 10-18 | 10-19 | 10-20 | 10-21 | 10-22 | 10-23 | 10-24 | 10-25 | 10-26 | 10-27 | 10-28 | 10-29 | 10-30 | 10-31 | 11-01 | 11-02 | 11-03 | 11-04 | 11-05 | 11-06 | 11-07 | 11-08 | 11-09 | 11-10 | 11-11 | 11-12 | 11-13 | 11-14 | 11-15 | 11-16 | 11-17 | 11-18 | 11-19 | 11-20 | 11-21 | 11-22 | 11-23 | 11-24
Actual | 13.4 | 14 | 22.6 | 23.9 | 23.5 | 25.2 | 14.5 | 14.9 | 14.7 | 23.1 | 24 | 22.3 | 22.5 | 24.4 | 13.5 | 12.9 | 23 | 22.4 | 24.1 | 22.9 | 22.6 | 14 | 14 | 22.5 | 24.6 | 22.2 | 23.2 | 22.3 | 14.8 | 15.6
Forecast | 15.6 | 23.3 | 23.3 | 23.4 | 23.4 | 23.5 | 12.7 | 12.8 | 23.3 | 23.3 | 23.3 | 23.3 | 23.4 | 12.7 | 12.8 | 23.2 | 23.2 | 23.3 | 23.3 | 23.4 | 12.6 | 12.7 | 23.2 | 23.2 | 23.2 | 23.2 | 23.3 | 12.6 | 12.7 | 23.1 | 23.1
Accuracy 97.6% · dips are weekends and holidays · +1 °C ≈ +935 kWh/day

## Slide 10: REST API and security
How a user logs in and gets data
Login
username + password
JWT token
valid 30 minutes
API request
token sent in header
Role check
admin / facility / student
GET /api/analytics/overview/ → KPIs and carbon totals
GET /api/analytics/live/ → live building status
GET /api/analytics/forecast/ → 30-day forecast
PATCH /api/alerts/12/ → resolve an alert
GET /api/reports/ghg.pdf → download PDF report

## Slide 11: Frontend: the web dashboard
13 pages
Dashboard, energy, water, waste, alerts…
Live updates
React Query refreshes every 30 s
Charts & map
Recharts + Leaflet / OpenStreetMap
Responsive
Works on laptop and phone
Built with React 19 + TypeScript, bundled by Vite

## Slide 12: Testing and results
18 / 18
automated tests pass
6 / 6
faults detected
97.6%
forecast accuracy
0.2 s
API response time
Chart: Campus emissions by source, last 30 days (tCO2e)
| Canteen & labs (LPG) | Waste disposal | Water supply & treatment | Campus fleet | Student & staff commuting | Purchased electricity
tCO2e | 4 | 5 | 5 | 10 | 208 | 424
7,975
tonnes CO2e per year
1.53 t per student
Electricity is about two-thirds

## Slide 13: From sensor readings to climate action
IoT data in → carbon, alerts and forecasts out
Python + Django REST API with a GHG carbon engine
Automatic anomaly detection and demand forecasting
React dashboards for admins, facility staff and students
Next: real ESP32 meters, MQTT and AI-based AC control
Thank you
Questions welcome